## Slide 1: CF34-10 LPT Case MRB (SONR HA24K230405) Deformation Check
IHI Co. Confidential
IHIQST-23-0331
01.06.2023

## Slide 2: Evaluation List for LPT Case MRB
LPT Shroud/Nozzle Installation Check – Case Hook Diameter
Stg.1 LPT Shroud Fit Check – Case Hook Thickness/Groove Depth
Stg.2, 3 LPT Shroud Fit Check – Case Hook Axial Runout
RSP.I Diameter Check around Fwd Flange and Case Thickness Check
Aft Flange ID Check
Anti-rotation pin position nonconformance is evaluated in other study.

## Slide 3: Overview of Case CMM data locations 1
236
（106）
237
(107)
238
(109)
239
(108)
240
(111)
241
(113)
242
(115)
243
(114)
244
(117)
245
(119)
246
(121)
247
(120)
248
105
 | Shroud |  |  |  | Nozzle |  | 
 | Stg.1 | Stg.2 | Stg.3 | Stg.4 | Stg.2 | Stg.3 | Stg.4
Fwd Hook Base Dimension Location | 105 | 238 | 242 | 246 | 237 | 241 | 245
Aft Hook Base Base Dimension Location | 236 | 240 | 244 | 201 | 239 | 243 | 247
Tolerance [mm] (Dwg.) | +/-0.082 | +/-0.064 | +/-0.064 | +/-0.0575 | +/-0.064 | +/-0.064 | +/-0.064
101, 201
(Aft Flange ID)
* No in parentheses shows runout

## Slide 4: Overview of Case CMM data locations 2
Axial Runout Check1 (112)
(Stg.2 LPT Shroud Aft Hook)
Axial Runout Check2 (118)
(Stg.3 LPT Shroud Aft Hook)
LPT Case
Thickness Check (225 - 207, 226 - 207)
Stg.1 LPT Shroud
LPT case Hook Thickness Check (234 - 235)
Stg.1 Shroud Fit Check (105 - 235)
112
118
309
342
207 (RSP.I)
226
225 (RSP.I)
105
235
234

## Slide 5: Overview of Case CMM data locations (Engine Manual limit)
237
239
241
243
245
247
EM Dia DE
EM Dia DE + 2 x Dim DN
EM Dia DD
EM Dia DD + 2 x Dim DM
EM Dia DC
EM Dia DC + 2 x Dim DL
 |  | Stg.2 NZL |  | Stg.3 NZL |  | Stg. 4 NZL | 
 | Location | 237 | 239 | 241 | 243 | 245 | 247
EM Limit (Avg. Dia.) | O/Max | 0.101 | 0.709 | 0.097 | 0.225 | 0.196 | 0.068
 | U/Min | 0.317 | 0.445 | 0.333 | 0.543 | 0.412 | 0.152
Engine Manual Limit |  | Dia. | Dim. | Dia. + 2 x Dim.
Stg.2 (Dia. DE/Dim DN) | Max | 722.965 mm | 15.654 mm | 754.273 mm
 | Min | 722.419 mm | 15.286 mm | 752.991 mm
Stg.3 (Dia. DD/Dim DM) | Max | 793.961 mm | 10.664 mm | 815.289 mm
 | Min | 793.403 mm | 10.495 mm | 814.393 mm
Stg.4 (Dia. DC/Dim DL) | Max | 838.860 mm | 0.180 mm | 838.832 mm
 | Min | 838.124 mm | -0.014 mm | 838.484 mm

## Slide 6: (1) LPT Shroud/Nozzle Installation Check Case Hook Diameter

## Slide 7: Stg.1 Shroud Dimensions of Steps
H6.0cm x L7.95cm
H11.2cm x L14.85cm
236
105
Hook radius profile
Shroud positions of parts
Shroud profile of step dimensions
f712.60+/-0.1
Shroud組み付け時の傾き(段差)
Unit mm
Judgment
O/Max 0.021 at Loc.18(11 o'clock at ALF.).
O/Max is within max acceptance limit.
Red arrow shows rotation direction of stg.1 Shroud at Loc.18.

## Slide 8: Stg.2 Shroud Dimensions of Steps
Hook radius profile
Shroud positions of parts
238
240
Shroud組み付け時の傾き(段差)
Unit mm
H11.2cm x L14.85cm
H6.0cm x L7.95cm
Shroud profile of step dimensions
Judgment
Within Limit.

## Slide 9: Stg.3 Shroud Dimensions of Steps
Hook radius profile
Shroud positions of parts
242
244
Shroud組み付け時の傾き(段差)
Unit mm
H11.2cm x L14.85cm
H6.0cm x L7.95cm
Shroud profile of step dimensions
Judgment
Within Limit.

## Slide 10: Stg.4 Shroud Dimensions of Steps
Hook radius profile
Shroud positions of parts
Shroud組み付け時の傾き(段差)
Unit mm
H11.2cm x L14.85cm
H6.0cm x L7.95cm
Shroud profile of step dimensions
201
246
Judgment
O/Max 0.041 at Loc.23(11 o'clock at ALF).
O/Max is within max acceptance limit.
Red arrow shows rotation direction of stg.4 Shroud at Loc.23.

## Slide 11: Stg.4 Shroud Dimensions of Steps (Shroud Backplate Interference)
Hook radius profile
Shroud positions of parts
Shroud組み付け時の傾き(段差)
Unit mm
H11.2cm x L14.85cm
H6.0cm x L7.95cm
Shroud profile of step dimensions
246
248
Judgment
Within Limit.

## Slide 12: Stg.4 Shroud Fwd Hook
246
2.0+/-0.13
Aft Flange ID (246) = f835.3+/-0.064
Aft Hook Dia. OD = f839.3+/-0.324
Hook Thickness = Avg. 2.03 (S/N:JHV419BJ Measurement Data)
Base = 246 with Hook Avg. Thickness at fwd side
Base = 246 with Hook Avg. Thickness at aft side
Dimensions are within dwg. limit
R O/Max | 0 | -
R U/Min | 0 | -
R O/Max | 0 | -
R U/Min | 0 | -

## Slide 13: Stg.4 Shroud Aft Hook
201
201 – Tool Max/Min Dimensions
1.5+/-0.05
Aft Flange ID (201) = f844.936+/-0.051
Aft Hook Dia. OD = f841.936+/-0.151
Tool dimension 1.5+/-0.03 is assumed after slot machining.
Tool Max Dimension 1.53
Tool Min Dimension 1.47
R O/Max | 1 | O/Max 0.017
R U/Min | 5 | U/Min 0.065
R O/Max | 5 | O/Max 0.076
R U/Min | 1 | U/Min 0.005

## Slide 14: Stg.4 Shroud Hook Step Evaluation
(201 – Tool Max) - (Loc. 246 + avg.2.03)
(201 – Tool Min) - (Loc. 246 + avg.2.03)
Radius Fwd/Aft Step = |½ (f839.3+/-0.324 ) – ½ (f841.936+/-0.151 )| =1.318+/- 0.2375

## Slide 15: Stg.2 Nozzle Dimensions of Steps
237
239
Hook radius profile
Nozzle positions of parts
Nozzle profile of step dimensions
Nozzle組み付け時の傾き(段差)
Unit mm
H6.0cm x L7.95cm
H11.2cm x L14.85cm
Judgment
Within Limit.

## Slide 16: Stg.3 Nozzle Dimensions of Steps
241
243
Hook radius profile
Nozzle positions of parts
Nozzle組み付け時の傾き(段差)
Unit mm
H11.2cm x L14.85cm
Nozzle profile of step dimensions
H6.0cm x L7.95cm
Judgment
Within Limit.

## Slide 17: Stg.4 Nozzle Dimensions of Steps
245
247
Hook radius profile
Nozzle positions of parts
Nozzle組み付け時の傾き(段差)
Unit mm
H11.2cm x L14.85cm
Nozzle profile of step dimensions
H6.0cm x L7.95cm
Judgment
U/Min 0.000 at Loc.3(1 o'clock at ALF).
U/Min is within min acceptance limit.
Red arrow shows rotation direction of stg.4 Nozzle at Loc.3.

## Slide 18: (2) Stg.1 LPT Shroud Fit Check Case Hook Thickness/Groove Depth

## Slide 19: LPT case Hook Thickness Check/Stg.1 Shroud Fit Check
f716.64+/-0.05
f709.5+/-0.064
Groove Depth for Stg.1 Shroud (Fit Check) ½ (f716.64+/-0.05) – ½ (f709.5+/-0.064)
– (2.02+/-0.025)
= 1.55 +/-0.082
#235
#105
Stg.1 Shroud Fwd Hook
#234
LPT case Hook Thickness Check ½ (f716.64+/-0.05) – ½ (f709.5+/-0.064)
= 3.57 +/-0.057

## Slide 20: CMM data plot #105, #234

## Slide 21: CMM data plot #235

## Slide 22: LPT case Hook Thickness Check (#234-#235)

## Slide 23: Stg.1 Shroud Fwd Hook Fit Check (#105-#235)
Fit Check at Fwd Side (#105 - #235_2001)
Fit Check at Aft Side (#105 - #235_2002)
Dimensions are within dwg. limit

## Slide 24: (3) Stg.2, 3 LPT Shroud Fit Check Case Hook Axial Runout

## Slide 25: Axial Runout Check Methodology
T : Hook Axial Thickness(CMM Max is used)
W : Shroud Groove Dwg. Min Width
振れ計測結果からShroud Segment位置の振れを内挿法により計算し、Segment間の振れ変化を差分にて評価する。
この差分評価の最大値が上図で示すMin Clearanceを超えなければ組付けは問題ないと判断する。
超える場合は回転による組付け性を考え回転量が微小量であることを確認する。
L : Shroud 1 segment (Circumferential Length)
d : LPT case hook runout
for shroud 1 segment
c : Max clearance between case hook and
shroud groove. c = W - T
Shroud Rotation Angle q = atan((d-c)/L)
q
q
T
W

## Slide 26: Axial Runout Check 1 (112) – Stg.2 LPT Shroud Aft Hook

## Slide 27: Axial Runout Check 2 (118) – Stg.3 LPT Shroud Aft Hook

## Slide 28: (4) RSP.I Diameter Check around Fwd Flange and Case Thickness Check

## Slide 29: Fwd Flange ID (#207 RSP.I)
Actual CMM data
After data processing with Least-Square Method

## Slide 30: Point Diameter (#225 RSP.I)
Actual CMM data
After data processing with Least-Square Method

## Slide 31: OD #226
Actual CMM data
After data processing with Least-Square Method

## Slide 32: LPT Case Thickness Check

## Slide 33: (5) Aft Flange ID Check

## Slide 34: Aft Flange ID (#101, 201)
101: Aft Flange ID Plot
201: Aft Flange ID Roundness
If both avg. diameter and roundness (shown as “runout” in table) of 201 meet drawing limits (“-” in table), nonconformance of 101 can be accepted.
Note:
CMM data of 101 has a tendency to be u/min due to insufficient fixture and limited measurement points.
Although CMM data of 201 is measured under free state condition, more measurement points than 101 trace actual deformation of LPT case correctly. Avg. diameter check is based on engine manual limit.
Copyright © 2022 IHI Corporation All Rights Reserved.

## Slide 35: Reference only: Radius difference between front and rear on hooks

## Slide 36: Radius difference between front and rear on hooks
H11.2cm x L16.15cm
Hook radius profile
Hook radius differences
Unit mm
238
242
246
Pos1
Pos2
Pos1
Pos2
Pos1
Pos2
Stg2
Stg3
Stg4
0.11 mm
Radius difference between front and rear |  |  | 
 |  | Rear-Front | Area#
238 | max | 0.019 | 11
 | min | 0.004 | 2
242 | max | 0.018 | 10
 | min | 0.002 | 3
246 | max | 0.013 | 6
 | min | -0.001 | 3
＋：front<rear、-：front>rear |  |  | 

## Slide 37: Summary
Shroud and Nozzle installation | Dimension of step evaluation meeting DWG requirement | Slide no.
Stage 1 shroud | No | 7
Stage 2 shroud | Yes | 8
Stage 3 shroud | Yes | 9
Stage 4 shroud | No | 10
Stage 4 shroud Backplate Interference | Yes | 11
Stage 2 Nozzle | Yes | 15
Stage 3 Nozzle | Yes | 16
Stage 4 Nozzle | No | 17
All step dimensions between fwd. and aft hook are within drawing requirement, Except Stg1, 4 Shrouds and Stg4 Nozzle. So clearance study may be required.

## Slide 38: CF34-10 LPTCASE RCR判定 しきい値一覧
This document and any files transmitted with it contain IHI proprietary information and are confidential hence are intended solely for the use of the individual or entity to whom they are addressed. Any disclosure, reproduction, distribution or other dissemination or use of this communication is strictly prohibited without the express permission of the sender. If you are not the intended recipient, please do not read, copy or disclose this communication. Please also notify the sender of the mistake by replying to this message and delete this message from your system.
Y. Okaniwa TSD
（AESJ-6228-008） 左記番号では登録されていない
02.16.2022

## Slide 39: Summary
目的
検査適正化に伴い、LPT CASEの遡及処置を行い、公差緩和を実施する。本検討では、公差緩和前にRCR判定手続きを行うため、RCR判定子と該当箇所を明確にする。
・RCR判定該当箇所：
直径寸法公差：検査項目番号・平均径・最大最小径を示す。（全17箇所）
・RCR判定方法
直径寸法公差：CF34-8のRCR化と同様平均径・最大最小径を用いたlimit値を用いる。
結論：
直径寸法：RCR判定を実施する。（全17箇所） CF34-8と同様 平均径・最大最小径を用いたしきい値(本文p.4)
※Interface寸法(#225)については、都度PIN合意もしくはrepeat pinの合意が必要のため今回のRCR判定処理からは除外する。
RCR化の期間：図面改訂が完了するまでの間実施予定
今後の流れ
1.RCR判定の検査項目箇所・最大最小径・平均径のlimit値を送付 act.岡庭
2. RCR判定のしきい値をSONRに登録するための保留起票（ダミー)を別で行う。
検査場への指示：品管から検査場への連絡をする
※shaft等での前例有

## Slide 40: Location
CF34-10 LPT CASE (2226M37)
FWD Flange
※Interface寸法（#225）
RCR判定処理をしても図面要求から逸脱した場合PIN合意を得なければならない。
(o/max側のrepeat pinを提出する必要がある)

## Slide 41: RCR判定 Limit値
最大・最小径及び平均径を使用しLimit値とする。
Ref.AESJ-6226-006rev.Bの値を使用
遡及処置時の値は公差緩和量よりも大きいものを含む
また、遡及処置時に公差緩和量±0.18mm以下の箇所については、遡及処置時の値を使用する。
（段差・板厚についての追加要求を含めていないため、実績がある値までとする）
chr.No. | DWG req | 最大・最小径 | 従来図面からの外れ | 平均径
 | Nominal | Tolerance +/- | O/Max,U/Min | Tolerance +/-
 | [mm] | [mm] | [mm] | [mm]
234 | 716.64 | 0.18 | 0.13 | 0.05
235 | 709.5 | 0.18 | 0.116 | 0.064
236 | 718.8 | 0.18 | 0.116 | 0.064
237 | 722.8 | 0.18 | 0.116 | 0.064
238 | 749.1 | 0.18 | 0.116 | 0.064
239 | 753.5 | 0.18 | 0.116 | 0.064
240 | 789.8 | 0.18 | 0.116 | 0.064
241 | 793.8 | 0.18 | 0.116 | 0.064
242 | 811 | 0.18 | 0.116 | 0.064
243 | 815 | 0.17 | 0.106 | 0.064
244 | 834.6 | 0.136 | 0.072 | 0.064
245 | 838.6 | 0.086 | 0.022 | 0.064
246 | 835.3 | 0.18 | 0.116 | 0.064
247 | 838.7 | 0.18 | 0.116 | 0.064
248 | 839 | 0.18 | 0.116 | 0.064
101 | 844.936 | 0.18 | 0.129 | 0.051
226 | 724.85 | +0.22/-0.13 | - | -
※Interface寸法(#225)
RCR判定処理をしても図面要求から逸脱した場合PIN合意を得なければならない。
(o/max側のrepeat pinを提出する必要がある)
今回のRCR化からはからは除外

## Slide 42: appendix

## Slide 43: Appendix 遡及処置時の値
chr.No. | Location | Nominal | Tolerance | O/max from DWG req | U/min from DWG req
 |  | [mm] | [mm] | [mm] | [mm]
234 | Stg.1 Shroud Fwd Hook OD | 716.64 | ±0.05 | 0.181 | -0.217
235 | Stg.1 Shroud Fwd Hook ID | 709.5 | ±0.064 | 0.185 | -0.281
236 | Stg.2 Nozzle Fwd Hook ID | 718.8 | ±0.064 | 0.175 | -0.285
237 | Stg.2 Nozzle Fwd Hook OD | 722.8 | ±0.064 | 0.287 | -0.26
238 | Stg.2 Nozzle Aft Hook ID | 749.1 | ±0.064 | 0.157 | -0.277
239 | Stg.2 Nozzle Aft Hook OD | 753.5 | ±0.064 | 0.197 | -0.47
240 | Stg.3 Nozzle Fwd Hook ID | 789.8 | ±0.064 | 0.204 | -0.193
241 | Stg.3 Nozzle Fwd Hook OD | 793.8 | ±0.064 | 0.191 | -0.101
242 | Stg.3 Nozzle Aft Hook ID | 811 | ±0.064 | 0.203 | -0.147
243 | Stg.3 Nozzle Aft Hook OD | 815 | ±0.064 | 0.13 | -0.17
244 | Stg.4 Nozzle Fwd Hook ID | 834.6 | ±0.064 | 0.126 | -0.136
245 | Stg.4 Nozzle Fwd Hook OD | 838.6 | ±0.064 | 0.086 | -0.072
246 | Stg.4 Nozzle Aft Hook ID | 835.3 | ±0.064 | 0.145 | -0.195
247 | Stg.4 Nozzle Aft Hook OD | 838.7 | ±0.064 | 0.185 | -0.462
248 | Stg.4 Shroud Aft Hook ID | 839 | ±0.064 | 0.189 | -0.184
101 | Aft Flange ID | 844.936 | ±0.051 | 0.233 | -0.18
225 | OD Point(RSP.I) | 725.4 | ±0.13 | 0.085 | -0.378
226 | Fwd Slope End OD | 724.85 | ±0.13 | 0.293 | -0.297